## Slide 1
01 SYSTEM OVERVIEW
One vehicle history becomes one traceable maintenance action
The model ranks risk. The rule engine checks whether the evidence is stable enough to act.
5
risk classes
C0 to C4
4
risk horizons
6 / 12 / 24 / 48
1
stored decision
latest active vehicle row
Risk48
Risk24
Risk12
Risk6
Readouts
Temporal features
XGBoost
Action
FleetCare AI / Group 47 / Technical walkthrough
0:00–0:30
01
Notes: The five-class model outputs class probabilities and four cumulative horizon risks. The dashboard reads the stored latest decision and does not rerun the model.

## Slide 2
02 MODEL ITERATION
The experiments progressively removed leakage, weak history signals and cost dependence
Twelve experiment stages converged on vehicle-aware temporal XGBoost with no cost objective.
00
Static baseline
Random Forest
03
Nonlinear ranking
XGBoost
05C
Vehicle split
Leakage control
08
Past-only history
Rates + change
11
Policy rules
Persistence
12C
Final search
25 combinations
FINAL DESIGN
XGBoost
vehicle-level split
past-only temporal features
no cost objective
FleetCare AI / Group 47 / Technical walkthrough
0:30–1:15
02
Notes: Experiment sequence from repository test_00 through test_12c. Cost-based selection was removed because the public data does not contain an operational cost model.

## Slide 3
03 MODEL SELECTION
Twenty-five feature and parameter combinations produced two final models
One model ranks near-term risk. The other produces the five-class state.
FEATURE SET
F1 all rates
F2 rates + change
F3 short rates
F4 long rates
F5 rates + short change
25
combinations
screened on PolicyDev
PARAMETER SET
P1 regularized
P2 shallow
P3 medium
P4 very shallow
P5 less regularized
RISK RANKING
F5 + P3
Mean horizon AP 0.192 ± 0.014
FIVE-CLASS STATE
F5 + P5
Macro F1 0.202 ± 0.004
FleetCare AI / Group 47 / Technical walkthrough
1:15–2:00
03
Notes: User-provided test_12c output. F5 with P3 medium selected for horizon risk ranking. F5 with P5 less regularized selected for five-class classification.

## Slide 4
04 MODEL EVALUATION
Accuracy remains high because C0 dominates; Macro F1 and AP reveal the hard part
Official Validation provides an independent diagnostic after PolicyDev model selection.
97.0%
overall accuracy
Useful for completeness, but dominated by C0
Chart: 
| F5 + P3 | F5 + P5
Macro F1 | 0.2011 | 0.2035
Mean horizon AP | 0.04028 | 0.043174
Official Validation, five-seed mean
Macro F1
0.203
five-class balance
Mean horizon AP
0.043
minority-risk ranking
Risk6 AP
0.032
immediate-risk ranking
Decision signal
Use Macro F1 and horizon AP
when comparing models
FleetCare AI / Group 47 / Technical walkthrough
2:00–2:45
04
Notes: Official Validation means: accuracy 0.970, Macro F1 approximately 0.203, mean horizon AP 0.043 for F5/P5, and Risk6 AP 0.032. Accuracy is dominated by the majority C0 class.

## Slide 5
05 RULE ENGINE
History and stability checks stop noisy class jumps from becoming maintenance actions
Risk escalation starts only after the prediction passes the evidence gates.
MODEL
OUTPUT
History?
Stable?
Risk?
ACTION
TRD
COLLECT MORE DATA
one readout
TR0 / TRV
MANUAL REVIEW
short or unstable history
SEVERITY
TR1
PRIORITY INSPECT
C4 + extreme Risk6 + persistence
TR2/3
INSPECT
C3/C4 + Risk12 or persistent Risk6
TR4
ENHANCED MONITOR
C2 or Risk24 + trend
TR5
MONITOR
C1 or Risk48 + trend
TR6
CONTINUE
no combined evidence
Evidence required before escalation
class + horizon risk + recent vehicle history
FleetCare AI / Group 47 / Technical walkthrough
2:45–3:35
05
Notes: TRD handles vehicles with only one readout. TR0 and TRV route insufficient or unstable histories to manual review. TR1 through TR6 use class, horizon risk, persistence and deterioration evidence.

## Slide 6
06 PRODUCTION SCRIPT
The batch script scores the latest available vehicle history and stores the result once
The dashboard reads the latest active row. New readouts trigger the next batch run.
fleetcare_inference.py
features
model · SHAP · rules
PostgreSQL
truck + readouts
Model artifacts
model + schema
PostgreSQL public
analysis + prediction_shap
Dashboard
latest active row
run_model.py
CLI entrypoint
193,095
readouts
5,037
predictions
7
collect more data
verified dry run
FleetCare AI / Group 47 / Technical walkthrough
3:35–4:20
06
Notes: Sources: SystemCode/data/run_model.py and SystemCode/data/fleetcare_inference.py. Verified dry run: 193,095 readouts, 5,037 predictions and 7 COLLECT_MORE_DATA vehicles. Dashboard query filters isactive = 1 and in_maintenance IS NULL.