## Slide 1
FLEETCARE AI
Model Iteration,
Evaluation and
Decision Logic
SCANIA Component X predictive maintenance
Final model, temporal rules and production inference
Intelligent Reasoning Systems Project
Notes: Sources: project model outputs and final inference code. Cover artwork generated for this presentation as a technical illustration, not a photograph of a real vehicle.

## Slide 2
Model iteration
Six experiment stages led to the final no-cost XGBoost design
02
01
Random Forest
Latest-state baseline exposed severe class imbalance
02
XGBoost
Nonlinear five-class probabilities improved flexibility
03
Vehicle-aware split
Vehicle separation prevented leakage across observations
04
Temporal features
Rates, changes and past-only history used repeated readouts
05
Policy experiments
Calibration, cost and capacity rules were tested
06
Final search
Feature and parameter selection used no operational cost target
Final direction
XGBoost with vehicle-aware history; cost-based selection removed because the public dataset has no operational cost model.
FLEETCARE AI / INTELLIGENT REASONING SYSTEMS
Notes: Sources: experiment sequence test_00 through test_12c. Cost experiments were reviewed but excluded from final no-cost model selection.

## Slide 3
Feature and parameter search
Five feature collections were screened against five XGBoost configurations
03
Set | Feature collection | Purpose
F1 | Rate, all horizons | Broad temporal baseline
F2 | Rate + change, all | Adds absolute historical movement
F3 | Short rates | Focuses on 6 and 12-unit windows
F4 | Long rates | Focuses on 24 and 48-unit windows
F5 | Rates + short changes | All rates plus 6 and 12-unit changes
SEARCH DESIGN
25
feature / parameter
combinations
5
random seeds
42, 52, 62, 72, 82
RISK RANKING
F5 + P3 medium
FIVE-CLASS CLASSIFICATION
F5 + P5 less regularized
FLEETCARE AI / INTELLIGENT REASONING SYSTEMS
Notes: Source: test_12c_feature_parameter_search.py. P3: 250 estimators, learning rate 0.05, depth 5. P5: 250 estimators, learning rate 0.05, depth 4 with lower regularization.

## Slide 4
Final model evaluation
PolicyDev selected the configurations; Official Validation stayed outside model selection
04
Chart: 
| F5 + P3 | F5 + P5
Macro F1 | 0.2011 | 0.2035
Mean horizon AP | 0.04028 | 0.043174
Official Validation, five-seed mean
POLICYDEV WINNERS
0.192 ± 0.014
Mean horizon AP
F5 + P3 medium
0.202 ± 0.004
Macro F1
F5 + P5 less regularized
Accuracy 0.970
Macro F1 0.203
Accuracy is dominated by C0. Macro F1 and horizon AP better reflect minority-risk performance.
FLEETCARE AI / INTELLIGENT REASONING SYSTEMS
Notes: User-provided test_12c results. Official Validation: F5/P3 Macro F1 0.201098, mean horizon AP 0.040280; F5/P5 Macro F1 0.203502, mean horizon AP 0.043174. PolicyDev winners: risk-ranking mean AP 0.192175 ± 0.014271; five-class Macro F1 0.201593 ± 0.003539.

## Slide 5
Temporal rule engine
Probabilities and recent history produce a stable maintenance action
05
RELIABILITY SAFEGUARDS
Rule | Condition | Action
TRD | Only one readout | COLLECT_MORE_DATA
TR0 | C3/C4 with fewer than three historical readouts | MANUAL_REVIEW
TRV | Low confidence and repeated large class jumps | UNSTABLE / MANUAL_REVIEW
MAINTENANCE DECISION LADDER
Rule | Core condition | Action
TR1 | C4 + extreme Risk6 + persistence or deterioration | PRIORITY_INSPECT
TR2 / TR3 | C3/C4 + extreme Risk12, or extreme persistent Risk6 | INSPECT
TR4 | C2, or high Risk24 with persistence or deterioration | ENHANCED_MONITOR
TR5 | C1, or high Risk48 with persistence or deterioration | MONITOR
TR6 | No combined evidence for escalation | CONTINUE
FLEETCARE AI / INTELLIGENT REASONING SYSTEMS
Notes: Source: SystemCode/data/fleetcare_inference.py. Current thresholds: Risk48 P80, Risk24 P85, Risk12 P90 and Risk6 P95 for high-risk evidence; TR1 and TR2 use P99.5 escalation evidence. TR0 precedes TRV.

## Slide 6
Production inference script
The model creates one latest decision per vehicle and stores it for the application
06
01
PostgreSQL
truck_readout + truck
02
Feature engineering
current, rate, change, history
03
Final XGBoost
P(C0...C4) and four horizons
04
Rule engine
TR0-TR6, TRV and TRD
05
Stored output
analysis + prediction_shap
06
Backend
latest row per active vehicle
RUN COMMAND
.venv/bin/python -u SystemCode/data/run_model.py
One readout bypasses the model and receives COLLECT_MORE_DATA.
VERIFIED DRY RUN
193,095
readouts
5,037
model predictions
7
collect-more-data
Dashboard query: latest analysis row per vehicle; isactive = 1; in_maintenance IS NULL.
FLEETCARE AI / INTELLIGENT REASONING SYSTEMS
Notes: Sources: SystemCode/data/run_model.py, SystemCode/data/fleetcare_inference.py and verified dry-run output. The dry run produced one latest prediction for 5,037 vehicles and seven COLLECT_MORE_DATA decisions without database writes.