## Slide 1
FLEETCARE AI
Model Iteration, Evaluation
and Decision Logic
SCANIA Component X predictive maintenance
Final model, temporal rule engine and production inference
Five-class probability model with Risk6, Risk12, Risk24 and Risk48
Intelligent Reasoning Systems Project
C4
Risk6
TR1
Notes: Sources: project model outputs and final inference code in SystemCode/data/fleetcare_inference.py.

## Slide 2
Model iteration
Each iteration addressed a specific limitation found in the previous experiment
01
Random Forest
Latest-state baseline
Exposed class imbalance
02
XGBoost
Nonlinear five-class
probabilities
03
Vehicle-aware
Vehicle split and
past-only temporal features
04
Multi-readout
Rates, changes and
historical windows
05
Policy trials
Calibration, cost and
capacity experiments
06
Final search
No-cost feature and
parameter selection
Final direction
The project retained XGBoost with vehicle-aware history. Cost-based model selection was removed because the public dataset does not provide an operational cost model.
FleetCare AI
02
Notes: Sources: model experiment sequence in repository history: test_00, test_01, test_02-05, test_06c-10c, test_11c and test_12c. Cost experiments were reviewed but excluded from the final no-cost selection objective.

## Slide 3
Feature and parameter search
Five feature collections were screened against five XGBoost configurations
Set | Feature collection | Purpose
F1 | Rate, all horizons | Broad temporal baseline
F2 | Rate + change, all | Adds absolute historical movement
F3 | Short rates | Focuses on 6 and 12-unit windows
F4 | Long rates | Focuses on 24 and 48-unit windows
F5 | Rates + short changes | Keeps all rates and adds 6/12-unit changes
Search design
25
feature / parameter combinations
in the first screening round
5
random seeds for finalists
42, 52, 62, 72, 82
Risk ranking
F5 + P3 medium
Five-class classification
F5 + P5 less regularized
FleetCare AI
03
Notes: Source: test_12c_feature_parameter_search.py on the model branch. P3: 250 estimators, learning rate 0.05, depth 5. P5: 250 estimators, learning rate 0.05, depth 4 with lower regularization.

## Slide 4
Final model evaluation
PolicyDev selected the configurations. Official Validation remained excluded from model selection
Chart: 
| F5 + P3 | F5 + P5
Macro F1 | 0.2011 | 0.2035
Mean horizon AP | 0.04028 | 0.043174
Official Validation, five-seed mean
PolicyDev winners
0.192 ± 0.014
Mean horizon AP
F5 + P3 medium
0.202 ± 0.004
Macro F1
F5 + P5 less regularized
Accuracy 0.970
Macro F1 0.203
High accuracy mainly reflects the dominant C0 class. Macro F1 and horizon AP provide a more honest view of minority-risk performance.
FleetCare AI
04
Notes: User-provided results from test_12c. Official Validation: F5/P3 Macro F1 0.201098, mean horizon AP 0.040280; F5/P5 Macro F1 0.203502, mean horizon AP 0.043174. PolicyDev winners: risk-ranking mean AP 0.192175 ± 0.014271; five-class Macro F1 0.201593 ± 0.003539. Earlier Official Validation accuracy mean 0.970194 and Macro F1 mean 0.202518.

## Slide 5
Temporal rule engine
The model supplies probabilities. Deterministic rules convert evidence into maintenance actions
Reliability safeguards
TRD
1 readout
COLLECT MORE DATA
TR0
C3/C4 + <3 history
MANUAL REVIEW
TRV
low confidence + repeated jumps
UNSTABLE
MANUAL REVIEW
Maintenance decision ladder
TR1
C4 + Risk6 top 0.5% + persistent / fast
PRIORITY INSPECT
TR2 / TR3
C3/C4 with extreme Risk12, or extreme persistent Risk6
INSPECT
TR4
C2, or high Risk24 with persistence / deterioration
ENHANCED MONITOR
TR5
C1, or high Risk48 with persistence / deterioration
MONITOR
TR6
No combined evidence for escalation
CONTINUE
Volatility safeguard: confidence < 0.35, probability margin < 0.03, and at least three class jumps of two or more levels within the recent five predictions.
FleetCare AI
05
Notes: Source: SystemCode/data/fleetcare_inference.py. Current thresholds: Risk48 P80, Risk24 P85, Risk12 P90 and Risk6 P95 for high-risk evidence; action escalation for TR1 and TR2 uses P99.5. TR0 precedes TRV in rule order.

## Slide 6
Production inference script
The application reads stored results. The model runs only when operational data changes
PostgreSQL
truck_readout
truck
Feature engineering
current, rate, change
rolling history
Final XGBoost
P(C0…C4)
Risk6/12/24/48
Rule engine
TR0–TR6
TRV and TRD
Stored output
analysis
prediction_shap
Backend
latest row
per vehicle
Run command
.venv/bin/python -u SystemCode/data/run_model.py
Each vehicle receives one latest decision. Vehicles with one readout bypass the model and receive COLLECT_MORE_DATA.
Verified dry run
193,095
readouts loaded
5,037
latest model predictions
7
collect-more-data decisions
Dashboard queries filter to the latest analysis row per vehicle, then exclude inactive or in-maintenance vehicles.
FleetCare AI
06
Notes: Sources: SystemCode/data/run_model.py, SystemCode/data/fleetcare_inference.py and verified dry-run output from 8 October 2026. Dry run produced one latest prediction for 5,037 vehicles and seven COLLECT_MORE_DATA decisions, without database writes.